## Slide 1
STA1 / SESSION 1
Data and
Descriptive Statistics
How to describe an observed engineering sample
250 µm
a target is useful—
but it is not the whole story
CENTRE • SPREAD • SHAPE • PATTERN
22-SLIDE STANDALONE DECK

## Slide 2
OPENING / RUNNING EXAMPLE
02 / 22
A running example: plate thickness
STA1 • DATA AND DESCRIPTIVE STATISTICS
CONTEXT
An inline sensor records 180 manufactured plates.
MEASURE
Thickness in micrometres (µm); target = 250 µm.
STRUCTURE
Production line A or B; sample ID preserves production order.
FOUR QUESTIONS
1 What value is typical?
2 How much do values vary?
3 What is the distribution shape?
4 Do line or order patterns stand out?

## Slide 3
OPENING / SCOPE
03 / 22
Description comes before inference
STA1 • DATA AND DESCRIPTIVE STATISTICS
01
DESCRIPTIVE STATISTICS
What do these 180 observed measurements look like?
02
INFERENTIAL STATISTICS
What might the wider production process be like?
This session stays with description: centre, spread, shape, potential outliers and visible patterns.

## Slide 4
FOUNDATIONS / SCOPE
04 / 22
Population, sample, parameter and statistic
STA1 • DATA AND DESCRIPTIVE STATISTICS
POPULATION
All units or measurements of interest.
SAMPLE
The units or measurements actually observed.
PARAMETER
A numerical summary of a population.
STATISTIC
A numerical summary calculated from a sample.
POPULATION
observed
sample

## Slide 5
FOUNDATIONS / VARIABLES
05 / 22
Each variable has a role
STA1 • DATA AND DESCRIPTIVE STATISTICS
Q
QUANTITATIVE
thickness_um
A continuous measurement. Mean, median, standard deviation and quartiles are meaningful.
C
CATEGORICAL
line
A label: A or B. Compare counts or the two observed distributions.
#
ORDER / INDEX
sample_id
Production sequence. Useful for detecting drift; not itself a physical measurement.

## Slide 6
SECTION 01
01
Represent the sample
Tables, plots and numerical summaries
06 / 22

## Slide 7
REPRESENTATION / FREQUENCY
07 / 22
One frequency table, three graphical views
STA1 • DATA AND DESCRIPTIVE STATISTICS
FREQUENCY TABLE
Count how often each observed value occurs.
Salary (×1000 DKK) | Frequency
37 | 4
38 | 1
39 | 3
40 | 5
41 | 8
42 | 10
44 | 5
46 | 2
47 | 3
50 | 1
VERTICAL LINES
FREQUENCY POLYGON
Chart: 
| 37 | 37
37 | 0 | 4
38 | 0 | 1
39 | 0 | 3
40 | 0 | 5
41 | 0 | 8
42 | 0 | 10
44 | 0 | 5
46 | 0 | 2
47 | 0 | 3
50 | 0 | 1
Chart: 
| 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
Frequency | 4 | 1 | 3 | 5 | 8 | 10 | 0 | 5 | 0 | 2 | 3 | 0 | 0 | 1
BAR GRAPH
Chart: 
| 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
Frequency | 4 | 1 | 3 | 5 | 8 | 10 | 0 | 5 | 0 | 2 | 3 | 0 | 0 | 1
Horizontal: salary (×1000 DKK) • Vertical: frequency

## Slide 8
REPRESENTATION / PLOTS
08 / 22
Histograms group measurements into intervals
STA1 • DATA AND DESCRIPTIVE STATISTICS
CONSTRUCTION
Choose measurement intervals (bins), then count the observations in each.
AXES
Horizontal: measurement intervals.
Vertical: frequency or relative frequency.
WHY BIN WIDTH MATTERS
Wide bins hide detail; narrow bins can emphasise noise.

## Slide 9
REPRESENTATION / CENTRE
09 / 22
Centre answers “What is typical?”
STA1 • DATA AND DESCRIPTIVE STATISTICS
x̄
MEAN
Uses every value. Useful for roughly symmetric data, but sensitive to extremes.
Q₂
MEDIAN
The middle ordered value. Resistant to extremes and useful for skewed data.
Mo
MODE
The most frequent value or category. It may be absent or non-unique.

## Slide 10
REPRESENTATION / CENTRE
10 / 22
One extreme value can move the mean
STA1 • DATA AND DESCRIPTIVE STATISTICS
ORIGINAL VALUES
7 9 11 12 13 15 17
17 → 117
MEAN 12 → 26.3
MEDIAN 12 → 12
The median depends on order; the mean is an arithmetic balance point.

## Slide 11
REPRESENTATION / SPREAD
11 / 22
Spread is about distance from the centre
STA1 • DATA AND DESCRIPTIVE STATISTICS
01
RANGE
maximum − minimum
quick, but controlled by two values
02
DEVIATION
xᵢ − x̄
one value’s signed distance from the mean
03
STANDARD DEVIATION
s
a typical distance, in the original unit
04
VARIANCE
s²
the corresponding squared measure
A process can be centred on target and still vary too much.

## Slide 12
REPRESENTATION / SPREAD
12 / 22
Sample variance uses n − 1
STA1 • DATA AND DESCRIPTIVE STATISTICS
SAMPLE VARIANCE
n
number of
observations
xᵢ
observation i
x̄
sample mean
n − 1 adjusts for estimating the unknown population mean from the same sample.

## Slide 13
REPRESENTATION / RESISTANT SPREAD
13 / 22
Quartiles describe the middle 50%
STA1 • DATA AND DESCRIPTIVE STATISTICS
Order the observations, then locate three landmarks.
IQR = Q₃ − Q₁
Q₁
25%
Q₂
50% / median
Q₃
75%
middle half of the observed sample
Quartile algorithms can differ slightly; state the convention when exact agreement matters.

## Slide 14
REPRESENTATION / POTENTIAL OUTLIERS
14 / 22
IQR fences flag potential outliers
STA1 • DATA AND DESCRIPTIVE STATISTICS
LOWER FENCE
Q₁ − 1.5 × IQR
UPPER FENCE
Q₃ + 1.5 × IQR
Potential outlier = an observation outside either fence
FLAG → INVESTIGATE → EXPLAIN
A flag is not an instruction to delete the observation.

## Slide 15
REPRESENTATION / BOXPLOT
15 / 22
A boxplot puts the summaries together
STA1 • DATA AND DESCRIPTIVE STATISTICS
BOX
Runs from Q₁ to Q₃; the centre line is the median.
WHISKERS
End at the lowest and highest observed values inside the fences.
DOTTED LINES
The 1.5×IQR outlier boundaries—not observed minima or maxima.
OUTSIDE POINTS
Potential outliers plotted individually.
Read from the centre outward:
median → box → whiskers → outside points

## Slide 16
SECTION 02
02
Interpret the pattern
Shape, groups and production order
16 / 22

## Slide 17
INTERPRETATION / SHAPE
17 / 22
The histogram shows the overall shape
STA1 • DATA AND DESCRIPTIVE STATISTICS
LOOK FOR
01
one or several peaks
02
symmetry or skewness
03
concentration and spread
04
gaps and extreme values
WORKED EXAMPLE
180 observed plates; dashed line = 250 µm target

## Slide 18
INTERPRETATION / SHAPE
18 / 22
Skewness is named by the tail
STA1 • DATA AND DESCRIPTIVE STATISTICS
RIGHT SKEW
long tail toward higher values
SYMMETRIC
comparable tails
LEFT SKEW
long tail toward lower values

## Slide 19
INTERPRETATION / GROUPS
19 / 22
Compare groups with side-by-side boxplots
STA1 • DATA AND DESCRIPTIVE STATISTICS
LINE A
n = 90 median = 249.69 µm s = 4.16 µm
LINE B
n = 90 median = 250.86 µm s = 5.37 µm
In this observed sample, line B has the larger standard deviation.
That is not yet a population claim.

## Slide 20
INTERPRETATION / ORDER
20 / 22
Production order can reveal drift
STA1 • DATA AND DESCRIPTIVE STATISTICS
A histogram discards order.
A run plot preserves it.
LOOK FOR
a systematic rise, fall, shift or cycle
CAUTION
no obvious pattern is not proof of stability

## Slide 21
INTERPRETATION / PLOT CHOICE
21 / 22
Choose the plot that answers the question
STA1 • DATA AND DESCRIPTIVE STATISTICS
01
HISTOGRAM
What is the overall shape?
one quantitative variable
02
BOXPLOT
How do groups compare?
centre, spread and potential outliers
03
RUN / SCATTER
Does order or a relationship matter?
sequence or paired variables
The question and variable roles determine the plot—not habit.

## Slide 22
CONCLUSION / RESPONSIBLE DESCRIPTION
22 / 22
Describe the sample—then stop
STA1 • DATA AND DESCRIPTIVE STATISTICS
01
STATE THE SCOPE
what was measured, how many observations and which groups
02
REPORT CENTRE AND SPREAD
use measures that suit the observed distribution
03
DESCRIBE THE PLOTS
shape, potential outliers, group differences and order patterns
04
RESPECT THE BOUNDARY
do not turn a sample description into a population claim
Example: these 180 plates are centred near 250 µm; line B appears more variable in the observed sample.